## Slide 1
Leak Detection Techniques and Sources
Studies in the Uinta Basin

## Slide 2
Ground and aerial optical gas imaging studies
Notes: 2

## Slide 3
Emissions quantification studies
Notes: 3

## Slide 4
Topic 1: Lessons about effectiveness of
optical gas imaging in different conditions
Notes: 4

## Slide 5
Optical gas imaging cameras detect fewer leaks
in cold weather
Notes: 5

## Slide 6
Optical gas imaging cameras detect fewer leaks
in cloudy conditions
Notes: 6

## Slide 7
Optical gas imaging cameras detect fewer leaks
with more distance from the source
Distance of camera from tanks on well pad
No plumes
detected
Small
plume
Medium
plume
Large
plume
Notes: 7

## Slide 8
High-sensitivity mode makes a big difference
Notes: 8

## Slide 9
  Takeaways:
  OGI cameras detect emissions less well when it is cold and/or cloudy
  Users can compensate for non-ideal conditions by:
    Getting closer
    Stabilizing the camera
    Using high sensitivity mode
Notes: 9

## Slide 10
Topic 2: Important sources of organic compound emissions at well pads
Notes: 10

## Slide 11
Most emissions detectable from off-pad
come from tanks
Aerial
Ground
Notes: 11

## Slide 12
Tank emissions are highest, even when tank vents are routed to combustors
Notes: 12

## Slide 13
Significant differences were observed by company
Notes: 13

## Slide 14
Significant differences were observed by company
Scores for company F before tank improvements (pads with controlled tanks only): 0.60 plumes per pad, severity score of 2.2
Notes: 14

## Slide 15
Takeaways:
Tanks are typically the largest emission sources on well pads
  This is true even for tanks with combustors
Tank emissions make more ozone than other emission sources
Investment in better equipment to reduce leaks from tanks makes a big difference
Notes: 15

## Slide 16
Additional thoughts:
  Efforts to reduce emissions when conditions are right for winter ozone are extremely valuable
    Thus the ozone alert program
  Automated tank malfunction detection would be a lot more effective, and less expensive, than manual OGI surveys
Notes: 16

## Slide 17
Real-time methane detection works,
but up-front costs are high
https://www.quanta3.com/products.html
Notes: 17

## Slide 18
On-tank sensors with telemetry
may be cheaper and more effective
https://oleumtech.com/oleumtech-products/thief-hatch-switch
https://www.dwyer-inst.com/Product/HazardousRated/PressureTransmitters/SeriesISDP
Thief hatch closure sensor
Tank pressure sensor
Notes: 18

## Slide 19
On-tank sensors with telemetry
may be cheaper and more effective
https://www.alphasense.com/index.php/products/pid-air/
Low-cost, high-sensitivity non-methane organics sensor
Notes: 19

## Slide 20
Final takeaways:
  OGI isn’t a magic bullet. Use it prudently.
  Tanks are the big well-level emission source to worry about. Action to prevent tank emissions makes a big difference.
  In a time when fewer workers handle more and more wells, automation may be the Key.
Notes: 20

## Slide 21
Thank You
Funding provided by:
Uintah Impact Mitigation Special Service District
Utah Legislature
Bureau of Land Management
Utah Division of Air Quality
Environmental Protection Agency
Thanks to:
Many oil and gas companies for providing information and site access
Contact us:
seth.lyman@usu.edu
Our website: binghamresearch.usu.edu

## Slide 22
Notes: 22