## Slide 1
Basin-Wide Pollutant Emissions Estimates
Seth Lyman, Utah State University
John Lin, University of Utah
Huy Tran, Utah State University

## Slide 2
Methane emissions declined through 2020
Steady methane leak rate relative to gas production
Leak relative to energy production has declined by about 25% (because of transition to oil from gas)
Lin et al., 2021

## Slide 3
Measurement locations

## Slide 4
We used methane emission rates and correlations to determine NOx and organics emissions
Alkanes
Aromatics
Alcohols
NOy

## Slide 5
Emissions declined through 2020,
then took a big jump in 2021

## Slide 6
Increase in emissions may be related to
increase in energy production

## Slide 7
Correlations are unique
for different pollutant groups
(Spearman rank correlations)

## Slide 8
Regulatory inventory is much too high for NOx,
about right for VOC

## Slide 9
Air quality models
Box model

## Slide 10
Air quality models
3D photochemical model

## Slide 11
3D models mostly can’t produce winter ozone without juicing up the inventory
Matichuk et al., 2017

## Slide 12
3D models mostly can’t produce winter ozone without juicing up the inventory
Matichuk et al., 2017

## Slide 13
Box model shows 3D model output
produces plenty of ozone

## Slide 14
But that same output in the 3D model
doesn’t produce enough ozone!

## Slide 15
What is going on?
The evidence shows that:
Inventoried total VOC emissions are high enough, but
VOC levels in modeled air are way too low, so
That VOC must be going somewhere! Thus,
We conclude that 3D models must be failing to capture the inversion adequately, so the model is allowing too much pollution to escape.
  Other evidence confirms this
  Model chemistry may also need improvement

## Slide 16
Forcing model to match met measurements helps, but is hard/expensive
Preliminary work by Trang Tran, USU

## Slide 17
The End
Takeaways
More oil and gas means more emissions
What happened in 2021?
The DAQ inventory is pretty good for VOC, but needs source-specific tweaks, and is too high for NOx
Poor performance of 3D photochemical models is due to poor meteorology, and maybe poor chemical mechanism, not due to the inventory.
What to do next?
Hire a meteorologist and a new photochemical modeler
Continue and improve annual emissions estimates
This project was funded by:
Utah DAQ, Utah Legislature, and Uintah County SSD1

## Slide 19
2021 spike wasn’t due to contamination from a single nearby source

## Slide 20
Emissions declined through 2020,
then took a big jump in 2021

## Slide 21
Ozone and NOx decreased through 2020 also
Mansfield and Lyman, 2021
Trend is robust, even when accounting for meteorology

## Slide 22
A better method for estimating emissions?

## Slide 23
A better method for estimating emissions?

## Slide 24
NOx is important in late winter,
organics are important all winter
Publication in prep; credit: Marc Mansfield

## Slide 25
2021 spike appears to have impacted
the whole Basin
Horsepool
Castle Peak

## Slide 26
Sources of methane and non-methane organics
are not the same
Sources:
https://documents.deq.utah.gov/air-quality/planning/technical-analysis/DAQ-2020-004826.pdf
https://www.naesb.org/pdf2/wgq_bps100605w2.pdf

## Slide 27
Composition trends through 2020 reversed in 2021

## Slide 28
Regulatory inventory composition
seems about right, except for alcohols

## Slide 29
Natural gas emissions in the Uinta Basin
are relatively high
Several studies have shown production-normalized emissions of about 6-8%.
Nationwide average is about 2-3%
Omara et al., 2018
The Basin has:
Lots of older, low-producing wells
Lots of oil wells

## Slide 30
Estimation of annual methane emission rate,
Lin et al., 2021
Lin et al., 2021