## Slide 1: 2023 Utah Area Source Oil and Gas Emissions
Uinta Basin Ozone Working Group Dec 10th 2025

## Slide 2
Chart: Utah Gas Production
| 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024
 | 315197367 | 295825783 | 272977899 | 242560333 | 240049464 | 260849337 | 290849337 | 306395123
Chart: Utah Oil Production
| 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024
 | 34437937 | 37116941 | 36933100 | 31000896 | 35771472 | 45401917 | 56495618 | 65142296

## Slide 4: Gap Filling
Tank Control Effectiveness Adjustment
Incident Reports (Leaks) from DOGM
Gas Well Venting (Blowdowns)
Pipeline Blowdowns and Pigging
Chart: 2023 VOCs with Gap Filling 32,652
| dehydrators_c_voc | dehydrators_voc | fugitives_voc | pneucont_voc | pneupumps_voc | rice_voc | separators_voc | tanks_c_voc | tanks_water_voc | tanks_oil_cond_voc | truck_voc | well comp_voc | centrifuge_voc | solid_voc | water_voc | Sum of VOC As_Gas_Flare | Gap Filling
 | 0.15075 | 59.8751 | 10649.9322 | 1514.0109 | 405.5348 | 11984.7184 | 62.087 | 3.6715 | 405.8092 | 2146.3283 | 278.913 | 1285.8133 | 2.9653 | 0 | 1.6741 | 62.3465 | 3788

## Slide 5
Chart: Workbook State Jurisdiction Emissions Tons Per Year
| Number of Facilities | PM10 | PM25 | SOX | NOX | VOC | CO | CH2O
2017 | 3170 | 206.6404 | 206.6404 | 9.7187 | 4437.6639 | 34825.7859 | 44384.3681 | 247.8907
2023 | 3481 | 261.7436 | 261.7436 | 10.2333 | 4642.4544 | 28863.8305 | 47025.0091 | 153.1458

## Slide 6
Chart: 2023 State Workbook Jurisdiction Emissions Tons Per Year
| 2023 PM10 | 2023 PM25 | 2023 SOX | 2023 NOX | 2023 VOC | 2023 CO | 2023 CH2O
Carbon | 7.2296 | 7.2296 | 0.46422 | 308.5577 | 4171.2353 | 1020.2213 | 14.11
Daggett | 0.073129 | 0.073129 | 0.0057733 | 0.96222 | 14.1383 | 0.80826 | 0
Duchesne | 161.2311 | 161.2311 | 6.1438 | 2812.4726 | 12195.6534 | 31312.0517 | 83.1334
Emery | 0.12061 | 0.12061 | 0.009182 | 1.7285 | 568.5946 | 1.3602 | 0
Garfield | 0 | 0 | 0 | 0 | 45.5074 | 0 | 0
Grand | 4.6366 | 4.6366 | 0.23624 | 161.9353 | 849.1607 | 2816.6955 | 5.3645
Rich | 0 | 0 | 0 | 0 | 0 | 0 | 0
San Juan | 0.74137 | 4.6366 | 0.022874 | 12.6722 | 189.2447 | 390.5877 | 0.64244
Sanpete | 0.42539 | 0.74137 | 0.013764 | 7.4525 | 10.4554 | 20.2025 | 0.4379
Sevier | 0 | 0 | 0 | 0 | 0 | 0 | 0
Summit | 0.53615 | 0.53615 | 0.031163 | 15.4234 | 103.7595 | 308.5068 | 0.24235
Uintah | 86.7495 | 86.7495 | 3.3063 | 1321.2501 | 10716.081 | 11154.5751 | 49.2152

## Slide 7
Chart: 2017 Workbook VOCs 34,922
| dehydrators_c_voc | dehydrators_voc | fugitives_voc | pneucont_voc | pneupumps_voc | rice_voc | separators_voc | tanks_c_voc | tanks_water_voc | tanks_oil_cond_voc | truck_voc | well comp_voc | centrifuge_voc | solid_voc | water_voc | Sum of VOC As_Gas_Flare
 | 0.0089079 | 271.1921 | 4589.1933 | 2174.7795 | 182.4945 | 23507.6414 | 59.5534 | 0.32455 | 319.4229 | 2720.1284 | 632.5804 | 368.4665 | 0 | 69.8432 | 26.58 | 0
Chart: 2023 Workbook VOCs 28,864
| dehydrators_c_voc | dehydrators_voc | fugitives_voc | pneucont_voc | pneupumps_voc | rice_voc | separators_voc | tanks_c_voc | tanks_water_voc | tanks_oil_cond_voc | truck_voc | well comp_voc | centrifuge_voc | solid_voc | water_voc | Sum of VOC As_Gas_Flare
 | 0.15075 | 59.8751 | 10649.9322 | 1514.0109 | 405.5348 | 11984.7184 | 62.087 | 3.6715 | 405.8092 | 2146.3283 | 278.913 | 1285.8133 | 2.9653 | 0 | 1.6741 | 62.3465

## Slide 8
Chart: 2017 Workbook NOx 4,438
| dehydrators_c_nox | rice_nox | separators_nox | tanks_c_nox | well comp_nox | Sum of NOX As_Gas_Flare
 | 1.5138 | 2781.9651 | 1081.334 | 43.8137 | 529.0373 | 0
Chart: 2023 Workbook NOx 4,642
| dehydrators_c_nox | rice_nox | separators_nox | tanks_c_nox | well comp_nox | Sum of NOX As_Gas_Flare
 | 1.783 | 1477.2673 | 1128.8541 | 60.9308 | 1854.8714 | 118.7477