## Slide 1
Over the past few years, we have been seeing some interesting trends in the data.
Ozone and ozone precursor concentrations have been trending downward since 2010.

## Slide 2
Background ozone: Local concentration due to all worldwide sources: About 40 to 50 ppb in winter.
Two patterns:
Snow cover, strong inversions, concentrations above background when inverted.
No snow cover, weak inversions, concentrations below background when inverted.
Pattern 1. Seasons with snow. | Pattern 2. Seasons without snow. | Outlier. Fits neither pattern well, although there was plenty of snow.
2011 2013 2014 2016 2017 2019 2020 | 2012 2015 2018 | 2010

## Slide 3
Yearly exceedances have been trending down at a rate of about 4 per year.

## Slide 4
Interpolate all the data for a single season to the same inversion strength (15 °C/km, a moderate inversion).
Ozone concentration is trending down by 4.1 ppb per year.

## Slide 5
Average NOx concentration, including only non-inverted days.

## Slide 6
Average VOC trends, including only non-inverted days.
Uptick in 2019, 2020.

## Slide 7
TWO CAUSES:
Trends in industrial activity
Pollution controls
  2012-2015 Quad-O regs
  2012-2015 Glycol dehydrator emissions caps
  2016 Quad-Oa regs