## Slide 1: Notice to Lessees and Operators of Onshore Federal and Indian Oil and Gas Leases(NTL-4a)
Definitions
  “Avoidably lost” production – royalty obligation
  “Beneficial purposes” – no royalty obligation
  “Unavoidably lost” production – no royalty obligation
Authorized Venting and Flaring of Gas – no royalty obligation
  A. Emergencies – limited to 24 hours per incident and to 144 hours cumulative for the lease during any calendar month
  B. Well Purging and Evaluation Tests – limited to 24 hours
  C. Initial Production Tests – limited to 30 days or the production of 50 MMcf of gas
  D. Routine or Special Well Tests – covers well tests other than those cited above with BLM approval

## Slide 2: NTL-4a
Other Venting or Flaring
  Gas Well Gas – Gas well gas may not be vented or flared except where the loss is defined as unavoidably lost production or considered “Authorized venting and flaring of gas”
  Oil Well Gas – Oil well gas may not be vented or flared except where the loss is defined as unavoidably lost production, considered “Authorized venting and flaring of gas” under Section III, or approved by the BLM based on consideration of an evaluation report or action plan

## Slide 3: 2016 Waste Prevention Rule
Waste Minimization Plans to be submitted with APDs
Clarifying definitions of avoidable (royalty obligation) and unavoidably (no royalty obligation) losses
Gas capture requirements
Provisions targeting methane emissions (pneumatic equipment, storage vessels, leak detection and repair (LDAR))
The 2016 Rule also revised BLM’s royalty-rate provision (§ 3103.3-1) to conform to statutory authority and established new royalty-free use provisions (subpart 3178)

## Slide 4: 2016 Waste Prevention Rule
Routine Venting and Flaring from Oil Wells
Measure and report volumes of gas vented or flared
Capture for sale or using on the lease a percentage of gas production.
  90% in 2020
  95% in 2023
  98% in 2026
Capture targets can be met on lease-by-lease basis, county-by-county, or state-by-state basis.
Exemptions if targets would impose such costs as to cause the operator to cease production and abandon significant recoverable oil reserves under the lease.

## Slide 5: 2016 Waste Prevention Rule
Equipment Requirements
Pneumatic controllers and pumps
  Low-bleed or no-bleed pneumatics
  zero-emission pumps, or route exhaust to processing equipment
Storage Vessels
  Route vapor to sales line if PTE ≥ 6 tpy VOC
Well Maintenance and Liquids Unloading
Reduction of waste from drilling, completion, and related operations.
  capture, use, flare, or inject gas that otherwise would be released during drilling and completion operations.

## Slide 6: 2016 Waste Prevention Rule
Leak Detection and Repair
Implement a Leak Detection and Repair (LDAR) program
Consistent with EPA’s 0000a
Semi-annual inspections at well sites, quarterly inspections at compressor stations.
Repair leaks within 30 days and verify leak is fixed.

## Slide 7: Replacement Rule
When the loss of oil or gas is avoidable or unavoidable
Avoidably lost production determination is like NTL-4A
Unavoidably lost production determination more defined than NTL-4A
Venting limitations
Gas-well gas may not be vented – requirement to flare

## Slide 8: Replacement Rule
Authorized Flaring and Venting of Gas
Initial production testing, 30 days or 50MMcf
Subsequent well tests, limited to 24 hours
Emergencies, limited to 24 hours, “temporary, infrequent and unavoidable situation”
Downhole well maintenance and liquids unloading, limited to 24 hours of venting or flaring with provisions
Oil-well gas venting and flaring is royalty free if rules, regulations, orders of applicable State regulatory agency or tribe are followed.
Notes: The following do NOT constitute emergencies
failure to install appropriate equipment of a sufficient capacity to accommodate the production conditions
failure to limit production when the production rate exceeds the capacity of the related equipment, pipeline, or gas plant, or exceeds sales contract volumes of oil or gas
scheduled maintenance - operator negligence, repeated equipment failures
≥ 3 emergencies within the past 30 days, unless BLM agrees emergencies could not have been anticipated or beyond operator’s control

## Slide 9: Regulatory History
NTL-4A – came into effect in 1981 until 2017
2016 Rule – parts became effective beginning January 2017, replaced in November 2018
Replacement Rule – came into effect November 2018 and overturned by court in July 2020
2016 Rule – would have gone into effect October 2020 but overturned by court.
NTL-4A – currently in effect.
Notes: Need guidance from HQ to know what rule was in effect between July and October 2020.

## Slide 10: Additional Information
Additional information on waste prevention rules - https://www.ndoil.org/wp-content/uploads/2019/02/BLM-Waste-Prevention-Royalties-Conservation_Feb_2019.pdf
NTL-4A implementation guidance - https://www.blm.gov/sites/blm.gov/files/energy_noticetolessee4a.pdf